TechNexion Software Loader Quick Start Guide
Version 2020.12.30.1

Quick Start Guide

# Overview
This document describes quick start guide to use the factory default TechNexion software loader to download and flash a demo operating system on TechNexion products.

# Supported Hardware
The factory default TechNexion Software Loader comes preloaded in:
- PICO-i.MX8M, PICO-i.MX8MM, PICO-iMX8MP (SOMs)
- FLEX-i.MX8MM, XORE-i.MX8MM, EDM-i.MX8M (SOMs)
- PICO-i.MX7D, PICO-i.MX6, PICO-i.MX6UL (SOMs)
- EDM-CF-IMX6 (SOM)
- TOUCAN0700, TOUCAN1000, (PANEL PCs)
- TEK-i.MX6 (BOX PCs)
- TEP5-i.MX6-10inch, TEP5-i.MX6-15inch (PANEL PCs)
- TEP1-i.MX7 (PANEL PCs)
Alternatively the factory default TechNexion Software Loader can be flashed directly to eMMC on TechNexion SOMs, or to a SD card which is used to boot TechNexion Box/Panel PC products.

# Download the factory default TechNexion Software Loader system
The factory default TechNexion Software Loader system should come preloaded into your development board. If not, please visit TechNexion’s download page to obtain a copy appropriate for your TechNexion target device:
ftp://ftp.technexion.net/factory_default_reset/
Once downloaded the a suitable TechNexion Software Loader (e.g. rescue-20201230.xz), please extract the xz file to an image file suitable for flashing to eMMC or SDcard. (e.g. in Ubuntu terminal: $ xz -d rescue-20201230.xz)
# Flashing the image into eMMC
There are two methods of flashing an image into eMMC of TechNexion SOMs.
A.) Using UUU tool
Please See YouTube Video and follow the Programming Process[1]:
[1] TechNexion Software Loader is an image build-able using yocto build environment. E.g. bitbake tn-image-tsl-fitimage
https://www.youtube.com/watch?v=vhicE5dNt30

B.) Using UMS u-boot command
Please See YouTube Video:
https://www.youtube.com/watch?v=eGXE0HFmTtE

# Flashing the Image into SD Card
If your PC runs Windows OS:
1. Unzip the win32diskimager.zip

2. Execute Win32DiskImager.exe.
3. Prepare a microSD card. Insert this microSD card into the card reader of PC.
4. Choose microSD you inserted for the “Device” drop-down choice.

5. Select the extracted “rescue.img” for the “Image File” input box.
6. Then, click “Write” button. Win32DiskImager will flash TechNexion Software Loader image into SD card.
If your PC runs Ubuntu OS:
1. Prepare a microSD card. Insert this microSD card into the card reader of PC.
2. Use ‘dd’ command to flash factory default TechNexion Software Loader image into microSD Card.
$ sudo dd if=rescue.img of=/dev/sd<disk> bs=1M oflag=dsync

# Setup Boot Mode to boot from eMMC or SD Card on target board
Switch the boot mode to boot from the baseboard SD card or module eMMC to run the factory default TechNexion Software Loader. The factory default TechNexion Software Loader will install from available OS image on TechNexion Software Loader web server into eMMC of your target SOM.

# Running the Factory Default TechNexion Software Loader (with GUI)
After power cycle the target board, GUI version of factory default TechNexion Software Loader system automatically starts up. If a display panel is attached to the target board, the GUI client for the TechNexion Software Loader system will display on the panel.

Please see YouTube video:
https://www.youtube.com/watch?v=nXTpUe0oT8Q

NOTE: If you do not have a display, and wishes to use command line interface to flash an OS image, then please skip to chapter 8.
# Factory Default TechNexion Software Loader in CLI
1. Make sure you connect a debug console to your target development board.
2. In your debug console, log in to the TechNexion Software Loader with user ‘root’ and no password.
3. Issue following commands,

# cd /usr/lib/python3.5/site-packages/rescue_loader
# ./installer.py
or
# python3 installer.py

4. Follow the command line prompts to flash a suitable OS image to a target storage on your target development board.

# Useful Links
TechNexion Software Loader file server: http://rescue.technexion.net/images/

# Known Issue:
1. Occasionally the TechNexion Software Loader’s installer daemon server will request and retain too much memory. And cause the Kernel to kill the process due to Out Of Memory (OOM). The TechNexion Software Loader is restored when this happens and can be restarted after reboot. If all attempts to download and program an OS failed using the TechNexion Software Loader. You may choose to issue following commands from the debug console to flash a desired image from TechNexion file server.
$ wget -q -O - URL-to-download-file.xz | xzcat | dd of=/dev/mmcblkX
where URL-to-download-file.xz is located in http://rescue.technexion.net/images/

2. The Font size on some panels may appear small and thin.

3. The TSL will boot and try to use all display panels connected to the target device.